## Slide 1: An introduction to MPEG transport streams
all you should know before using TSDuck

## Slide 2: Agenda
Transport streams
  packets, sections, tables, PES, demux
DVB SimulCrypt
  architecture, synchronization, ECM, EMM, scrambling
Standards
  MPEG, DVB, others

## Slide 3: packets and packetization
transport streams

## Slide 4: Standard key terms
Service / Program
  DVB term : service
  MPEG term : program
  TV channel (video and / or audio)
  data service (software download, application data)
Transport stream
  aka. « TS », « multiplex », « transponder »
  continuous bitstream
  modulated and transmitted using one given frequency
  aggregate several services
Signalization
  set of data structures in a transport stream
  describes the structure of transport streams and services

## Slide 5: MPEG-2 transport stream
Structure of MPEG-2 TS defined in ISO/IEC 13818-1
One operator uses several TS
TS = synchronous stream of 188-byte TS packets
  4-byte header
  optional « adaptation field », a kind of extended header
  payload, up to 184 bytes
Multiplex of up to 8192 independent elementary streams (ES)
  each ES is identified by a Packet Identifier (PID)
  each TS packet belongs to a PID, 13-bit PID in packet header
  smooth muxing is complex, demuxing is trivial
Two types of ES content
  PES, Packetized Elementary Stream : audio, video, subtitles, teletext
  sections : data structures

## Slide 6: Multiplex of elementary streams
A transport stream is a multiplex of elementary streams
  elementary stream = sequence of TS packets with same PID value in header
  one set of elementary streams for global signalization
    describe the TS, the network, the operator, the services, the events, EMM’s, etc.
  one set of elementary streams per service
    a service is typically a TV channel
global signalization streams
service 2 streams
service 1 streams
PMT
video
audio 1
audio 2
subtitles 1
subtitles 2
ECM 1
ECM 2
transport stream

## Slide 7: TS packet
47
header : 4 bytes
payload = 184 bytes
4-byte header includes :
Sync byte = 0x47
PID : 13 bits
Continuity counter : 4 bits
Payload Unit Start Indicator (PUSI) : 1 bit
Transport scrambling control : 2 bits
Adaptation field presence : 1 bit
Payload presence : 1 bit
More…
47
header : 4 bytes
payload < 184 bytes
adaptation field
TS packet without adaptation field
TS packet with adaptation field
adaptation field size
Adaptation field may include :
Program Clock Reference (PCR / OPCR)
Private data
Stuffing (for PES stream padding)
More…
AF = 1
AF = 0

## Slide 8: Multiplexing and demultiplexing
Elementary stream = concatenation of all payloads of all TS packets with same PID
Elementary stream transport
  packetization = cutting ES into packets payloads with same PID
    setting Payload Unit Start Indicator (PUSI) in TS header on « unit » boundary
  multiplexing = mixing with packets from other PID’s to build a complete TS
  demultiplexing = extracting all packets with same PID from TS
  depacketization = rebuilding ES from packets payloads with same PID
    using PUSI to resynchronize on « unit » boundary
Elementary stream :
Elementary stream :
TS packets :
packetization
depacketization

## Slide 9: Packetized Elementary Stream (PES)
A stream of PES packets
  up to 65536 bytes per PES packet
  start of PES packet identified by PUSI bit in TS header
PES packets can contain
  video : MPEG-2 (H.262), AVC (H.264), HEVC (H.265), etc.
  audio : MPEG-2 Layer 2, AAC, HE-AAC, AC-3, DTS, DTS-HD, etc.
  DVB subtitles (text or bitmap)
  teletext (deprecated but still used)
One elementary stream contains one single type of content
  video
  audio for one language (with or without « audio description »)
    multi-channel audio (stereo, 5+1, etc.) within same PID
  subtitles for one language (with or without « for hard of hearing »)
  exception : one teletext stream is a multiplex of several text streams (« pages »)

## Slide 10: Typical PES packetization
47
header
payload = 184 bytes
47
header
payload < 184 bytes
stuffing
adaptation field
PUSI = 1
47
header
payload < 184 bytes
PCR
adaptation field
(optional but typical)
PUSI = 0
PUSI = 0
00 00 01 …
PES packet start code prefix
First TS packet for PES packet
As many intermediate TS packets as required for current PES packet
(multiplexed with TS packets from others PID’s)
Last TS packet for PES packet
fill adaptation field with enough stuffing so that end of PES packet matches end of TS packet
PID = nn
PID = nn
PID = nn

## Slide 11: PES streams robustness
TS packet loss is tolerated in audio and video streams
  video « macro-block » effect
  audio « glitch » effect
  quality of recovery based on decoder implementation
TS packet loss detection based on continuity_counter
  4-bit field in TS packet header
  cannot detect loss of an exact multiple of 16 TS packets
  resynchronization on next TS packet with PUSI
But video / audio decoders can resynchronize within PES packet
  video / audio bitstream formats usually contain synchronization patterns
  example : NAL unit boundary in AVC encoding

## Slide 12: Sections streams
Contain data structures named « tables »
A table is split into one or more « sections »
  section = smallest data unit, up to 4096 bytes
  standard header and type-specific payload
  table type identified by table_id in header
  two types of section syntax : « short » and « long »
    based on 1 bit in header
Each type of table defines its own syntax
  use long or short sections
  payload bitstream syntax
Descriptor
  standard substructure with standard header and type-specific payload
  most tables use generic « lists of descriptors »

## Slide 13: Typical section packetization
47
header : 4 bytes
payload = 184 bytes
PUSI = 0
TS packet containing the start of section n+1
As many intermediate TS packets as required for section n+1
(multiplexed with TS packets from others PID’s)
Last TS packet for section n+1, start of next section
PID = nn
47
header : 4 bytes
payload = 184 bytes
PUSI = 1
PID = nn
pointer field (to first start of section)
end of section n
47
header : 4 bytes
payload = 184 bytes
PUSI = 1
PID = nn
pointer field
end of section n+1
continuation of section n+1
section n+2
start of section n+3
start of section n+1
table id
section size
table id
section size
table id
section size

## Slide 14: Tables with short section
One section per table
  section and table are equivalent
Each table brings new information
  CAS EMM / ECM
  date and time information (TDT / TOT)
No standard integrity check
  except section length in section header
  some table-specific mechanisms
    cryptographic integrity in EMM / ECM
    CRC32 in TOT

## Slide 15: Tables with long sections
Up to 256 sections per table
  need to receive all sections to rebuild the complete table
Same table repeatedly cycled
Content change notification
  version number in long section header
  each table is repeatedly broadcast with same version number
  version number changes when table content changes
  STB software sets demux filters to be notified of new tables only
Integrity check
  CRC32 in each section
  section rejected in case of corruption, can be detected at demux level
  resynchronization on next TS packet with PUSI

## Slide 16: Signalization: PSI / SI
MPEG-2
DVB (optional)
DVB (mandatory)
PSI : Program Specific Info.
  MPEG-defined
  ISO / IEC 13818-1
  TS structure: PAT, PMT
  CA : CAT
SI : Service Information
  DVB-defined
  ETSI EN 300 468
  private sections in MPEG terms
Extracted from DVB standard ETSI EN 300 468
schedule
EIT Other TS
present / follow
PID 18
EIT Actual TS
schedule
PID 18
Event Information
EIT Actual TS
present / follow
PID 18
TDT
PID 20
TOT
PID 20
Time & date
RST
PID 19
Running Status
SDT Actual TS
PID 17
SDT
Other TS
PID 17
Service Description
BAT
PID 17
Bouquet Association
NIT Actual Network
PID 16
NIT
Other Network
PID 16
Network Information
PAT
PID 0
CAT
PID 1
PMT
TSDT
PID 2

## Slide 17: MPEG-defined PSI
PAT : Program Association Table
  repeated in PID 0
  list of « services » in the TS, ie. TV channels or data channels
  service id and PMT PID
PMT : Program Map Table
  technical description of one service
  list of elementary streams in the service
    PID, type (audio, video, etc.), additional info using a list of descriptors
  list of ECM streams for this service
CAT : Conditional Access Table
  repeated in PID 1
  list of EMM streams on this TS
  CAT not present when no EMM on TS

## Slide 18: DVB-defined SI (1/2)
SDT : Service Description Table
  editorial description of the services in a TS
  either in « actual » TS or « other » TS
  service names and ancillary services
BAT : Bouquet Association Table
  commercial operator description and services
  several commercial operators may sell the same services
NIT : Network Information Table
  technical description of a network
  either « actual » network or « other » network
  list of TS in this network
    usually with frequency and tuning parameters
    used for fast network scanning
  list of services in each TS
    service ids and « logical channel number »

## Slide 19: DVB-defined SI (2/2)
EIT : Event Information Table
  editorial description of events
  either in « actual » TS or « other » TS
  EIT « present / following »
    short description of current and next event on each service
    used to display information banner on screen
  EIT « schedule »
    long description of all events in the forthcoming days
    used to display the EPG
    optional, depends on operator’s good will and bandwidth availability
    complete 7-day EPG for a large operator uses several Mb/s
    sparse EIT schedule sections, rarely complete tables
TDT / TOT : Time and Date Table / Time Offset Table
  current date and time, UTC (TDT) and local offset by region (TOT)
  used to synchronize STB system time
  typically one table every 10 to 30 seconds only

## Slide 20: one network, several conditional access systems
DVB SimulCrypt

## Slide 21: Standard key terms
CAS : Conditional Access System
CW : Control Word
  content encryption key for video & audio
EMM : Entitlement Management Message
  CAS-specific message to manage rights, smartcards, subscribers
  sent to some identified set of subscribers, possibly only one
ECM : Entitlement Control Message
  CAS-specific message to control a scrambled service
  sent to everyone willing to watch the service

## Slide 22: DVB SimulCrypt
Enforce coexistence of multiple CAS to protect the same content
  DVB-defined standard
Use-cases
  one broadcast operator, multiple commercial operators
  transition between CAS generations
Broadcast
  very simple architecture
  common scrambling
  multiple EMM and ECM streams with standard signalization
Head-end
  complex architecture
  multiple CAS equipment
  common synchronization

## Slide 23: DVB SimulCrypt head-end diagram
Extracted from DVB standard ETSI TS 103 197

## Slide 24: DVB SimulCrypt head-end
Interface between two worlds
  one « MUX system » vendor
    yellow components
  multiple CAS vendors
    blue components
DVB SimulCrypt protocols
  specified between components of distinct worlds
  protocols within the same world are not specified
    proprietary, vendor specific
  consistent nested tag-length-value (TLV) structures
    using logical « channels » and « streams »
    except ACG  EIS protocol (XML protocol)
  EIS  SCS protocol is specified
    so that EIS and SCS may in fact come from distinct vendors
TSDuck plugins
  scrambler interacts with any standard ECMG
  datainject interacts with any standard EMMG or PDG

## Slide 25: EMM signalization
Using CA_descriptor in the CAT of the TS
  standard part of CA_descriptor: CA system id, EMM PID
    CA_system_id are allocated by DVB
    http://www.dvbservices.com/identifiers/ca_system_id
  private part of CA_descriptor: CAS-specific
    used by the CA software in the STB
Number of EMM streams is CAS-specific
  for instance, one EMM stream may contain all EMM’s for
    one operator
    one EMM type (e.g. individual, group, global)
    or any other configuration
    when they exist, operator id and EMM types are CAS-specific concepts
    they are usually identified in the private part of the CA_descriptor

## Slide 26: ECM broadcast
An ECM usually transports a CW pair and access criteria
  specific to one or more audio or video streams
  specific to one CAS
Each service (i.e. channel) has dedicated ECM streams
  per scrambling group
  per CAS
    base mechanism for DVB SimulCrypt
Scrambling group
  a set of audio or video elementary streams scrambled with the same CW
  subtitles are usually not scrambled in practice (but could be in theory)
  usually, all audio and video streams of a service are in the same scrambling group
  in rare cases, audio and video streams are scrambled with distinct CW

## Slide 27: ECM signalization
Using CA_descriptor in the PMT of the service
  standard part of CA_descriptor : CA system id, ECM PID
    same as EMM signalization
  private part of CA_descriptor: CAS-specific
    used by the CA software in the STB
    CA_descriptor private part is usually different in CAT (EMM) and PMT (ECM)
    sample content : operator id, public subset of access criteria
Two possible positions for CA_descriptors in PMT
  at program level
    only if one single scrambling group
  at stream level
    mandatory if different ES use different CW
    take precedence over program level if both are used for same CA_system_id

## Slide 28: Scrambling synchronization (1/3)
During one crypto-period (CP) number N
  typically 10 seconds
  scrambling using same CWN
ECMN carries CWN and CWN+1
  initial ECM broadcast delayed from start of CP (CAS specific)
  ECMN is repeated several times during CPN (typically 10 ECM/s)
  if first ECMN+1 is missed, the descrambler already knows CWN+1 anyway
The CA software configures the descrambler with both CWN and CWN+1
  either N or N+1 is « even », the other one is « odd »
TS packet header contains 2-bit transport_scrambling_control
  used by the descrambler to select the appropriate CW
    00 : clear, do not descramble (MPEG-defined: ISO 13818-1)
    10 : use even CW (DVB-defined: ETR 289)
    11 : use odd CW (DVB-defined: ETR 289)
Implemented in TSDuck plugin scrambler

## Slide 29: Scrambling synchronization (2/3)
Based on crypto-period (CP) number
  CP numbers are sequentially allocated by SCS
  the full CP number stays on head-end
  its parity is used in TS packets and ECM’s
MUX / Scrambler
ECMG
TS packet
11
 transport_scrambling_control
scrambled with « odd » CW
ECM
BB..BB
CW :
AA..AA
even
odd
message CP num = 165 CW = AA..AA
CP num = 166 CW = BB..BB
message
parity = odd CW = AA..AA
CP number is odd
CWG
random stream
AA .. .. AA
BB .. .. BB
SCS
CP number is even
About to start
CP number 165

## Slide 30: Scrambling synchronization (3/3)
Crypto-periods timeline
Current CP number | 165 | 166 | 167
SCS → MUX | odd – AA..AA | even – BB..BB | odd – CC..CC
SCS → ECMG | 165 – AA..AA 166 – BB..BB | 166 – BB..BB 167 – CC..CC | 167 – CC..CC 168 – DD..DD
TS packet (t.s.c.) | 11 | 10 | 11
Scrambling CW | AA..AA | BB..BB | CC..CC
ECM (CW pair) |  |  | 
BB..BB
AA..AA
even
odd
BB..BB
CC..CC
even
odd
DD..DD
CC..CC
even
odd
≈ 10 seconds
time

## Slide 31: TS vs. PES scrambling
ISO 13818-1 defines two possible levels of scrambling
  TS level
    each TS packet is scrambled individually
    clear TS header and adaptation field, scrambled TS payload
  PES level
    each demuxed PES packet is scrambled individually
    TS packet header marked as clear
    PES packet header contains similar 2-bit PES_scrambling_control
    clear PES header, scrambled PES payload
In practice, only TS-level scrambling is used
  PES-level scrambling is technically much more difficult
    scrambling is performed on multiplexed TS
    ETR 289 specifies sub-scrambling of 184-byte super-blocks
    PES packet boundaries not aligned on crypto-period boundaries
  PES-level scrambling is never used in practice

## Slide 32: EMM & ECM tables
CA-private in DVB-defined range
  ETSI ETR 289 defines the range of private CA table ids
    0x80 – 0x81 : ECM
    0x82 – 0x8F : « CA private »
  defined as « short sections »
    no versioning
    each section is an independent new table
Typical usage
  0x80 and 0x81 alternating with crypto periods
    ECM table id change used as trigger by CA software to submit ECM to smartcard or TEE
    ECM table id and CP number do not necessarily have the same parity
  0x82 – 0x8F used for EMM’s
    CAS-specific
    typically one table id for each EMM type, easier to filter in STB

## Slide 33: Access criteria transition
Use case : restricted event or pay-per-view event transition
Scenario :
  the ECMG of each CAS had sent its own timing requirements to SCS
  SCS synchronizes the generation of the ECM from each CAS
Extracted from DVB standard ETSI TS 103 197

## Slide 34: Clear-to-scramble transition
Use case : Pay-TV channel with public periods in the clear
Scenario :
  the ECMG of each CAS had sent its own timing requirements to SCS
  SCS synchronizes the generation of the ECM from each CAS
Extracted from DVB standard ETSI TS 103 197

## Slide 35: DVB CSA-2
DVB Common Scrambling Algorithm
  DVB proprietary algorithm
  supposed to be « secret »
  fully described in Wikipedia
  open-source implementations online (libdvbcsa)
Algorithm
  64-bit key (also known as « Control Words » or CW)
  first pass : block cipher in reverse-CBC mode
    use CW as key
    block size : 64 bits
    residue ignored
  second pass : stream cipher
    use CW as key and first block as seed (last processed block from reverse-CBC)
    residue included
  short payloads (1 to 7 bytes) are not encrypted
    even if transport_scrambling_control is non-zero

## Slide 36: DVB CSA-2 entropy reduction
Entering the twilight zone….
64-bit key
  some national regulations from the 90’s prohibited 64-bit entropy
  entropy was artificially reduced to 48 bits
    cw[3] = (cw[0] + cw[1] + cw[2]) mod 256
    cw[7] = (cw[4] + cw[5] + cw[6]) mod 256
  entropy reduction is no longer required but still often applied
Operational issues
  hardware scramblers and descramblers use plain 64-bit keys
  CWG internally generates 64 random bits
  where is the entropy reduction applied ?
    common chain : CWG? SCS?
    scrambling chain : MUX? scrambler?
    descrambling chain : ECMG? smartcard? CA software in STB? descrambler?
    who knows if entropy reduction must be applied anyway?

## Slide 37: our essential references
Standards

## Slide 38: Essential standards
MPEG
  ISO 13818-1, MPEG-2 system layer (TS, packetization, PSI)
    transport stream  broadcast, blu-ray discs
    program stream  DVD
DVB / ETSI (Europe and more)
  EN 300 468, DVB service information specifications (signalization)
  TS 103 197, DVB simulcrypt head-end (CAS head-end)
ATSC (USA), ISDB (Japan, Brazil)
  equivalent features as defined in DVB

## Slide 39: Obtaining standards documents
ISO
  https://www.iso.org/standards.html
  must be purchased
DVB
  http://www.etsi.org/standards
  direct search : http://www.etsi.org/standards-search
  allocated identifiers : http://www.dvbservices.com/identifiers/
ITU
  http://www.itu.int/ITU-T/recommendations/
  H.xxx series : http://www.itu.int/rec/T-REC-H/
IETF
  https://tools.ietf.org/
NIST
  http://csrc.nist.gov/publications/

## Slide 40: Audio and video standards and nicknames
Origin | Type | ISO / IEC | ITU-T | Nicknames
MPEG-1 | Video | 11172-2 | H.261 | MPEG-1 video
MPEG-1 | Audio | 11172-3 |  | MPEG audio layer 1
MPEG-2 | Video | 13818-2 | H.262 | MPEG-2 video
MPEG-2 | Audio | 13818-3 |  | Layer 2: MPEG audio layer 2 Layer 3: MP3
MPEG-2 | Audio | 13818-7 |  | AAC (Advanced Audio Coding)
Dolby Digital | Audio |  |  | AC-3 (Audio Coding 3)
MPEG-4 | Video | 14496-2 | H.263 | DivX, Xvid (codecs)
MPEG-4 | Audio | 14496-3 |  | HE-AAC, EAAC (High Efficiency, Enhanced AAC)
MPEG-4 | Video | 14496-10 | H.264 | AVC (Advanced Video Coding)
MPEG-H | Video | 23008-2 | H.265 | HEVC (High Efficiency Video Coding)
Dolby Digital | Audio |  |  | AC-4

## Slide 41: Thank you