## Slide 1: TSDuck
A toolbox for MPEG/DVB transport streams
Thierry Lelégard IBC 2018, EBU Open Source Meetup

## Slide 2: What is TSDuck ?
A general-purpose toolbox for digital television engineers
  for MPEG transport streams (broadcast, IP-TV)
  flexible and extensible
Tools and plugins to be combined
  command line
  made for scripting
Linux, Windows, macOS

## Slide 3: TSDuck use cases
Digital television systems
  demo
  network monitoring
  system integration
  test
  debug
  lab activities in general

## Slide 4: TSDuck sample usages
  TS acquisition or transmodulation : satellite, terrestrial, IP …
  analysis : TS, PSI/SI, bitrates, timestamps …
  monitoring : bitrates, A/V properties, signalization, crypto …
  on-the-fly transformation or injection : content, PSI/SI …
  using and editing PSI/SI in XML or binary format
  modify, remove, rename, extract services
  inject or extract MPE, SCTE 35 splicing info
  extract T2-MI, teletext subtitles
  test bed for CAS or STB, scrambling and DVB SimulCrypt

## Slide 5: TSP – the transport stream processor
tsp process
tsp executable
packet processing plugin 2
packet processing plugin 1
packet processing plugin 3
input plugin
output plugin
input TS
output TS
    combination of elementary processing using plugins
    60+ standard plugins available

## Slide 6: TSP input / output plugins
Offline transport stream files
Re-route transport streams to / from other applications
Live transport streams
  UDP/IP, HTTP
  Specialized hardware
    cheap DVB tuners
    professional Dektec devices
    cheap HiDes modulators

## Slide 7: Sample MPE injection and extraction
MPE : Multi-Protocol Encapsulation
Media Server
Network 1
Linux or Windows
DVB
tuner
Linux or Windows
Dektec modulator
STB
STB
Multicast to
224.250.250.1 : 9000
Network 2
STB
STB
Multicast to
230.2.3.4 : 7000
STB
MPE encapsulation
inside existing TS
DVB
tuner
tsp
Modified destination
in UDP/IP datagrams:
230.2.3.4 : 7000
tsp

## Slide 8: Multiple TSP using merge and fork plugins
Merge with a TS coming from another application
  and merge signalization
Duplicate the TS to another application
tsp
input
input TS 2
output TS 2
plugin
merge
merge
plugin
fork
fork
output
tsp
input
plugin
plugin
file
tsp
input
plugin
plugin
file
input TS 1
input TS 3
tsp
file
plugin
plugin
output
tsp
file
plugin
plugin
output
output TS 1
output TS 3

## Slide 9: Conditional Access System test bed
DVB SimulCrypt interface
emulate CAS, test actual MUX
emulate MUX, test actual CAS
Linux or Windows
ECMG
EMMG
STB
tsp
DVB
tuner
Dektec
modulator
Linux, Windows
tsemmg
SCS
tsecmg
MUX

## Slide 10: Simple TSP examples
Transmodulation of a service over IP multicast
  tsp –I dvb –-uhf 35 -P zap france2 –-audio fra -O ip 224.10.11.12:1000
On-the-fly signalization replacement
  tsp -I dvb --uhf 24 -P inject nit.xml --pid 16 --replace –-stuffing -O dektec --uhf 24 --convolution 2/3 --guard 1/32
extract service « France 2 », keeping only one audio track
broadcast resulting SPTS to multicast IP address:port
replace content of PID 16 with table from XML file
send modified TS to a Dektec DVB-T modulator on same frequency

## Slide 11: TSDuck is extensible
Open source
    https://github.com/tsduck/tsduck
Design based on a large TSDuck library
  generic MPEG/DVB C++ library (400+ classes)
  common API for Linux, Windows, macOS
  programmer’s guide online
You may use this library to
  develop new plugins
  use in your own applications outside TSDuck

## Slide 12: https://tsduck.io/